## Slide 1
Internet Server Review
July 13, 1995

## Slide 2
Agenda
Status
  Performance
  Rollout
  Schedules
Open Issues

## Slide 3
Current Performance (Web)
* NCSA release 1.4 should be significantly faster

## Slide 4
Post-Beta Performance Work
AcceptEx(): Collapses accept(), ReadFile(), getsockname() into a single API consistant w/ NT async I/O model. Tuned for use w/ TransmitFile().
Caching user tokens
Coalesce heap allocations
Hotpath instruction tuning (system calls, LEGO, etc.)

## Slide 5
AcceptEx()
AcceptEx() + TransmitFile() changes saves:
  at least 8 kernel transitions
  3 heap allocations
  socket handle open/close
Expect ~30% performance benefit
  Initial tests show 100% improvement in traditional WinSock call path
Release plan: Fall NT SDK/CSD, notify NT Web vendors when code complete

## Slide 6
Rollout (Publishing)
www.microsoft.com
www.msn.net
Win95 launch event
  onsite dev support for Vivid (2 days)
25 internal Web server “experiments” (at least 3 BGI efforts underway)
Alpha (internal) release available end-of-week, expect 25 more users

## Slide 7
Catapult Rollout Status
2 systems running
  486/50 UP 32MB
  P90 QP 16MB
  average CPU load: 60-80%
July 11: 782 unique users, 350 unique sites, 140 peak concurrent users
Last week: 1189 total unique users, 6929 unique sites

## Slide 8
Catapult Rollout Status
ITG Meeting actions:
  Will limit Gauntlet to O’Hare test (bldg 5/6 only)+Telnet
  We will add ~120 VP-sponsored users to our pilot next week
  ITG will refer key users (w/ VP approval) to our Catapult pilot through ~8/15
  Following beta, ITG will begin to manage some servers, start killing direct taps (where not specifically needed)

## Slide 9
Development status
Approximately 2 weeks behind on schedules
Internal alpha release this week (publishing, setup, admin only)
O’Hare support in SmallProx
Web server-side include functionality added
Auto discovery next week

## Slide 10
Release Schedule (unchanged)
Stablization Periods
Beta1: 3 weeks
Beta 2: 3 weeks
Holidays: 2 weeks
RC: 6 weeks
RTM: 2 weeks
Schedule
Beta 1: 8/15/95
Beta 2: 11/1/95
RC1: 2/1/96
RTM: 2/15/96
Beta1 omitted functionality:
DNS editor, Catapult domain filtering, remote setup, unattended setup, Win95 admin tool, licensing, WfW discovery, BGI changes, DNS round-robin/perfmon/SNMP, generalized SmallProx
Beta2 full functionality

## Slide 11
Beta Plans
150 US, 150 International
  LORG/MORG40%, Solution Providers 20%, Service Providers 15%, ISV’s 15% SORG 10%
Schedule risks:
  WfW client (RPC issues)
  Discovery protocol (mileage)
  Full administration (mileage)

## Slide 12
SSL Update
X.509 certificate includes DNS name. Server gives RSA-signed certificate to client to create session keys. Client relies on DNS/IP to authenticate server. Cannot decrypt session w/o server private key, but may spoof server.
Not scheduled work, given a full SSPI/SSL provider probably 3 man-weeks in Web server code (+ test exposure)
Extensive work for SSL catapult support (effectively remotable WinSock)

## Slide 13
Open Issues
SSL
RealAudio
NNTP
Remotable WinSock
Exchange/Web
Native IPX support for publishing